[page 1]

Copy

Specification for building and finishing a

Dwelling House of one Storey at Park 1828

I. Mason Work.

The present House is proposed to be taken down and the new

one built upon its site, or a little to the rear of it, if the situation of the ground should

be preferable, the foundation to be dug so deep as to obtain good firm ground for

building upon – the House to be 45 Ft by 22 ½ Ft over the walls, the front and back

wall to be 2 Ft 3In thick and each of the Gables 21 Ft 6 In thick by 9 feet high in

the side wall above the top of the door sill, which is to be at least 6 in above the

level of the ground round the house. The foundation to be laid with broad flat stones

having a scarcement  of at least 4 in. on each side when the walls are sett off – That

part of the gables containing the fire places shall be five feet broad and project 9 in.

into the rooms, so as to have not less than 18 inches between the back of the flue

and the outside of the walls, but the projection may be cut off on reaching the

garret floor the floor to be not less than a foot in depth and from 12 to 15 inches

in width, built round a frame and carefully plastered. The corners rybats for

Doors and windows in the present house to be used in the new house and when

defficient, stones of a similar quality to be found by the Contractor. The

jambs and lintels and hearths to be polished freestone, the lintels to be 12 in. high and

together with the jambs, shewing at least 6 in. when finished. The hearths to be

12 in. longer than the chimneys, which shall not be less than 3 Ft wide – the

Lobby to be paved with freestone flags to be laid as well as the hearth with

lime mortar. – The window in the front wall to be 7 Ft. by 3 Ft the door 7 FT

by 3 Ft. 6 in. with a fan light above, the window in the garret 3 FT by 2 Ft  6 ins.

the chimney stalks to be at least 2 feet above the ridge of the roof and the top

or coping to be finished with a rounded stone, well jointed and projecting

at least three inches all round The skues to be freestone at least 15 in. broad.

by 2 ½ thick to project at least 2 in. and to overlap the slates three inches

and the chimney stalks to have water barges and proper raglings left for

the slater.

II. Carpenter Work.

The joists for the garret floor to be 9 in. by 2 ½ and sunk their

own depth into the wall of the House with a Crest of at least 9 in. or

each

[page 2]

each wall and not more than 18 inches apart. The roof to be framed 2 feet below the

square, the couple sides 7 in. at bottom and 6 in. at top by 2 ½ spicked to the joists

and a wall plate properly fixed to the wall – The earth to be taken out of

the area of the house to the depth of the foundation and the whole filled with stones

completely packed to prevent damp and exclude vermin and the top blinded with

lime riddlings, on which the sleeper joists of the two low rooms are to be laid

5 in. by 2 not more than 16 in apart and covered with flooring 1 inch thick

when finished, also the garret floor covered with boards 1 inch when dressed, to

be grooved and tongued, the whole to be well seasoned, no board to exceed

7 in. in breadth and to be free of sapwood. the roof to be sarked with

boards ¾ of an in. thick off the saw and half checked on each of the other half

an inch – The divisions to be lath standard 3 ½ by 2 in. not more than 14 in.

apart, the walls to be lathed on dooks fixed into the walls, the grounds 2 ½ by

¾ in. and not more than 14 in asunder, and lathed with strong split laths.

The four room doors to be bound and moulded on both sides, the press door

[page 3]

stair to have each a good lock – The outer door and windows and shutters

and press doors to have proper edge hinges and screws – the roof floors doors

etc to be of yellow American prime, the windows of the best Baltic:-

In case anything shall have been ommitted in the for-

going Specification, the Contractor shall have no claim on that

account for extra payment as it is understood by the proprietor that

the same is to be built and purchased by the Contractor in the

most substantial manner, and that hw is to deduct from the estimate

the value of the materials of the present house which may be

used for the new one.

The whole work to be finished in the month of July

1828 and to be harled in Sept[embe]r 1829. –